General Description:

Three Cylinder, Two Cycle, Bass Machines Tower & Lower Unit

Rated HP: 50 HP at 5,500 RPM, Racing @ 7,000 RPM

Displacement:   42.5 cu. in. (697cc), Bore & Stroke:  2.68 X 2.52 in. (68 x 64 mm)

Induction: 3-Carburetors, Loop Charged

Ignition System: Capacitor Discharge, One Coil per Cylinder

Water Pump: In Tower Housing Above Lower Unit

Lower Unit Prop Shaft Diameter: 11/16th in.

Shear Pin Hole: 1/4-in.

Available Gear Ratios: 17:17 or 16:17

Steering Bar, Fuel Connection Hose, Throttle Connection

Approximate Weight: 125-pounds

Fine Adjust Kick-Out And Height Bolt-On Transom Bracket (not in base price)

Welded Crank Pins (not in base price)

Purchase Options:

## Bass-Machines transom bolt-on system, add $350

## Bass-Machines welded crankshaft pins, add $500

- All prices are subject to change without notice

- Add packaging and shipping

- Add Washington State sales tax for Washington residents

The Bass Machines bolt-on transom bracket incorporates a fine adjustment for kick-out and engine height.  The engine may be purchased for the base price without a transom mounting system and the purchaser may use one of several brackets that use a 1-inch swivel pin.  For example, the MK 55H bracket can be used.  Other systems can be modified and used by the purchaser.  We recommend the Bass Machines variable adjustment bolt-on system be used for reasons of fine adjustment and operator safety.

Welding the crankshaft is a recommendation of Tohatsu America based on their experience racing this engine on rubber boats.  However, with the use of a racing lower unit and the resulting smaller propeller some have questioned if welding is necessary.  If the purchaser wishes to partially disassemble the engine and weld the crankshaft, basic written instructions will be provided.

# Delivery:

- 35% down, balance before delivery

- four to six months import and preparation required

Contact:

Sid Bass

## Phone (360) 373-3839

Bass Machines

2622 Rocky Point Road

Bremerton, WA 98312